## Slide 1
SDP Offline
Checkpoint Illustration
Document Version 2.4 (17 September, 2018)
Notes: 2009 Perforce User Conference
1

## Slide 2
SDP Physical Layout
/hxdepots/p4/acme/checkpoints
/hxdepots/p4/acme/depots
/hxdepots/p4/acme/bin
/hxdepots/p4/common/bin
Backup This Volume
/hxmetadata/p4/acme/root
/hxmetadata/p4/acme/offline_db
Do NOT backup metadata directly
/hxlogs/p4/acme/logs (journal)
Backup optional (Exclude Active Journal)
/p4 Contains mostly symlinks.
/p4/n
/OS
/hxlogs
Active Journal, various logs
/hxmetadata
Live & Offline db.*
/hxdepots
Versioned files, checkpoints, rotated journals
Animation Complete 
Notes: Animation!

## Slide 3
SDP Logical Layout (symlinks)
/hxdepots/p4/acme/checkpoints
/hxdepots/p4/acme/depots
/hxdepots/p4/acme/bin
/hxdepots/p4/common
/hxmetadata/p4/acme/root
/hxmetadata/p4/acme/offline_db
db.*, server.id, license
/hxlogs/p4/acme/logs
journal, log
/hxlogs/p4/acme/tmp
/p4/acme/
checkpoints
depots
bin
root
offline_db
logs
tmp
/p4/common

## Slide 4
SDP Offline Checkpoint Procedure
Key Features
No daily downtime.
Snapshot capability not needed on /hxmetadata.
Can use Snapshot capability /hxdepots volume.
Incorporates database integrity checks (not shown).
Occasional database regeneration.
  Requires only a few minutes of downtime when run.
  Does not require reset of attached replication.
  Usually run with p4d upgrades.
Works with older versions of p4d (99.1+?).
  Does not rely on new replication functionality
Notes: p4d 99.1 added ‘-z’ flag to –z. Tested as far back as 2005.x, but should work with older versions too.

## Slide 5
Sample Daily Procedure
Sp4d_1 -r /p4/1/root -J /p4/1/logs/journal –jj /p4/1/checkpoints/p4_1
Sp4d_1 -r /p4/1/offline_db -jr /p4/1/checkpoints/p4_1.jnl.3240
Sp4d_1 -r /p4/1/offline_db -jd -z /p4/1/checkpoints/p4_1.ckp.3241.gz
Initiate Snapshot and backup of /hxdepots volume.
srm –f /p4/1/offline_db/db.*
Sp4d_1 -r /p4/1/offline_db -jr -z /p4/1/checkpoints/p4_1.ckp.3241.gz
Note: With P4D 2018.1+, -z no longer needed; compress/uncompressed files can be in one call.
/hxmetadata
/p4/1/logs/journal
/p4/1/offline_db
/p4/1/root
/hxdepots
/p4/1/depots, checkpoints, etc.
/hxdepots
/p4/1/depots, checkpoints, etc.
d
p4_1.jnl.3240
p4_1.ckp.3241.gz
p4_1.jnl.3240
p4_1.ckp.3241.gz
Animation Complete 
Notes: Animation!
Snapshot will give ‘point-in-time’ consistent recovery of checkpoint and versioned files. This is only achievable in an enterprise environments if hardware-level snapshot capability is available.
Without point-in-time recovery, you still have consistent recovery, just archive files that are unknown to the database.
Stock recommendation: Use SAN for archive files to get data safety there, and modern replication for DR purposes.

## Slide 6
Sample Rebuild Procedure (On Demand)
p4d_1_init stop
p4d_1 -r /p4/1/root -J /p4/1/logs/journal –jj /p4/1/checkpoints/p4_1
p4d_1 -r /p4/1/offline_db -jr /p4/1/checkpoints/p4_1.jnl.3245
Swap out live and offline db.* files (mv root -> save, mv offline_db -> root).
p4d_1_init start
p4d_1 -r /p4/1/root/save -jd -z /p4/1/checkpoints/p4_1.ckp.3246.gz
Initiate Snapshot and backup of /hxdepots volume.
rm –f /p4/1/root/save/db.*
p4d_1 -r /p4/1/offline_db -jr -z /p4/1/checkpoints/p4_1.ckp.3246.gz
/hxmetadata
/p4/1/logsjournal
/p4/1/root
/p4/1/offline_db
/p4/1/root/save
/hxdepots
/p4/1/depots, checkpoints, etc.
/hxdepots
/p4/1/depots, checkpoints, etc.
d
p4_1.jnl.3245
p4_1.jnl.3246.gz
p4_1.jnl.3245
p4_1.jnl.3246.gz
db.*
db.*
Animation Complete 
Notes: Animation!
The Swap out procedure is instantaneous because ‘mv’ commands are instantaneous.
Downtime is mainly determined by the time it takes to replay just one day’s worth of journal data (typically a slow Saturday at that) into the offline_db. This should take just a few minutes.
Keeping root, save, and offline_db folders on the same volume is essential to the ability to regenerate databases routinely with minimal downtime.
We are exceedingly comfortable with this procedure. It has it has been in place at large sites for many years.

## Slide 7
Questions?
Notes: 2009 Perforce User Conference
7